## Slide 1: QD3000 Controller Setup Instructions
Navigate to Settings Pages 1 & 2
Scan the QR code above or click the link for basic settings and user preferences. Settings Pages can be easily toggled back and forth by the arrow in the bottom righthand corner.
Settings Page Overview

## Slide 2: QD3000 Controller Setup Instructions
Systems Settings 2 Specifics
1. If an electric eductor supply CAN valve is present inside the cabinet. Toggle this to GREEN. If no electric valve is present toggle the slider switch to RED.

## Slide 3: QD3000 Controller Setup Instructions
Older Style Small Valves set to the 1.5 Sec Default
Older Style Big Valves set to the 2.9 Sec Default
Newer Style Valves set to the 0.8 Sec Default
2. Valve close times can be adjusted based on Automated product valve size/type.
* Close Times for individual valves may vary – Fine tuning each will result in greater accuracy…

## Slide 4: QD3000 Controller Setup Instructions
Navigate to Advanced Settings.
Systems settings page 2 > Bottom of the screen > Click OK on the popup

## Slide 5: QD3000 Controller Setup Instructions
The Advanced Settings screen contains a combination of Soft Key Buttons, Modifiable Box Fields, Drop Down Boxes, and Slider Toggle Switches
5.A
5.D
5.E
5.F
5.B
5.G
5.C
Reference Page 5 for pages to follow.

## Slide 6: QD3000 Controller Setup Instructions
Carrier Meter type Identification
ARAG – Current Standard – Has LED Light
Seametrics – Previous Standard – has LCD screen
Polmac – Not Standard - Turbine Style
Tap this button to toggle choices
5.A

## Slide 7: QD3000 Controller Setup Instructions
Venturi vs Pump Suction Identification. Look behind the controller for electric valves, how many do you have?
Venturi model will have 2 electric valves
Pump Suction model will have 1 electric valve
Toggle to match your cabinet model.
5.B

## Slide 8: QD3000 Controller Setup Instructions
Verify your harness number on the white label where the harness connects to the controller.
QuickDraw Harness # | 208-05-5899Y1 | 208-05-4312Y2 | 208-05-4312Y1 | 208-05-2326Y5 | 208-05-2326Y4 | 208-05-2326Y1
Pressure Input Choice | QD3 | QD3 | QD3 | QD2 | QD2 | QD2
- How many Product valves does your cabinet have?
More than 1 if you’re blending different carriers.
Leave this active for best performance. Valve timing will auto adjust.
6
5.C
5.D
5.E
5.F

## Slide 9: QD3000 Controller Setup Instructions
Rinse valve identification and their connector types.
On the left is a normal valve type, has a 3-pin Weather Pack connector, and has a Yellow indicator for valve position.
On the right is a CAN valve type that has a visible LED light and a 4-pin Deutsch connector.
If you have the yellow valve type and the controller is set for Rinse Valve is CAN you will be in alarm an in an inoperable state.
5.G
5.G

## Slide 10: QD3000 Controller Setup Instructions
Once your controller is setup please navigate to the main MENU > RUN > MANUAL CONTROLS screen and individually check each electric valve to confirm proper function.
Operating System with Manual Controls